## Slide 1
GNSS Absolute Antenna Calibration at the National Geodetic Survey
Background
Gerald L Mader2 , Andria L Bilich1, Charles Geoghegan3 1National Geodetic Survey, NOAA/NOS, Boulder CO; corresponding author: andria.bilich@noaa.gov
1National Geodetic Survey, NOAA/NOS, Silver Spring, MD
3National Geodetic Survey, NOAA/NOS, Corbin VA
What is GNSS Antenna Calibration?
Antenna calibration = measurement of the antenna phase center (the apparent point of phase signal reception for a GNSS antenna)
Antenna phase center:
Differs between antenna models and manufacturers
Is affected by antenna radome and antenna mount
 | Relative | Absolute
Calibration values | Relative to a reference antenna (at NGS, use JPL chokering D/M_T) | Independent of reference antenna
Method | Stationary antennas | Test antenna moves
Advantages | Straightforward math | Sample full hemisphere and low elevation angles; independent of source
Limitations | Cannot sample full pattern; source-dependent | Requires robot and rigorous accounting of angles & rotations
Do not combine relative and absolute calibrations!
Relative vs. Absolute Calibration?
Advantages of absolute calibrations:
Better/fuller description of phase behavior
  Depends only on calibrated antenna (reference-free)
  Includes 0-10 elevation coverage
  Captures azimuthal variations
  Multipath removed/negated
The way of the future
  International GNSS Service (IGS) standard
  Used in OPUS and CORS multiyear
Compatible with absolute calibrations from any IGS-sanctioned facility
Serve high precision needs of U.S. surveying and geodesy communities
Multi-frequency, multi-GNSS calibrations
2-D (elevation, azimuth) phase center patterns
Free calibration service (antenna providers pay shipping)
Calibration values publicly distributed via Internet http://www.ngs.noaa.gov/ANTCAL/
Compatible with IGS ANTEX values
NGS Absolute Calibration
Motivation and Goals
To account for range errors introduced by the antenna element and hardware
Calibrations are a required input for many GNSS data processing packages
Omitting calibrations leads to estimation errors:
Long baselines
Combining multiple antenna models
Height errors
Why Do I Need Antenna Calibration?
Calibration values are given relative to a reference surface, typically the ARP
Method
Conclusions
Calibration
Setup
Flat field & concrete pad = well-behaved multipath environment
5 meter baseline (N-S orientation)
  precise baseline from survey
  baseline orientation used to fix robot reference frame
Data Reduction and Solution
Fixed reference antenna
Test antenna
The robot moves the test antenna between two closely spaced times. During that time interval the satellite has moved a negligible amount. Therefore multipath and PCO/PCV at the reference antenna are unchanged, and drop out when observations at the two times are differenced.
A full calibration is the sum of two different components:
  PCO (phase center offset)
    Point in space relative to physical, easily ID’ed and accessible ARP
    Given as NEU in antenna frame
  PCV (phase center variations)
    Relative to PCO
    Depends on direction of incoming satellite signal
N
S
E
W
References &
Acknowledgements
Bilich A and GL Mader, GNSS Antenna Calibration at the National Geodetic Survey, Proceedings of ION GNSS 2010, Portland, OR, September 2010, pp. 1369-1377.
The authors thank many people at NGS (Steven Breidenbach, Hong Chen, Kendall Fancher, David Geitka, Heeyul Han, Dennis Lokken, Frank Marion, Jaya Neti, Giovanni Sella, Bruce Tran, Jarir Saleh, and Mark Schenewerk) and the IGS Antenna Working Group (Ralf Schmidt, Phillip Zeimetz, Martin Schmitz for contributions to this project.
Please see our website at http://www.ngs.noaa.gov/ANTCAL for more information
  Robot
  2-axis pan and tilt unit
  rotation arm = 10.77 cm
  coincident origins for pan and tilt systems
  arm length and pan/tilt axis origin precisely measured with Total Station observations over range of robot pan/tilt angles
Antenna ARP ~ 50 cm above concrete pad (zero tilt)
10 cm Sokkia extension used to separate test antenna from robot
ARP (antenna reference point)
  Typically antenna mount point
  Defined by calibration facility
The NGS calibration facility is located in Corbin, VA.
Results
Topcon CR-G3
TPSCR.G3
N E U [mm]
IGS08 -0.17 0.30 88.41
NGS -0.23 1.50 87.76
N E U [mm]
IGS08 0.28 -0.04 119.40
NGS 0.26 0.83 118.20
s/n 0152
97% < 1mm @ >10
84% < 2mm @ 10
PCV
PCO
residuals
statistics
Favorable individual comparison to IGS published values and other calibration institutions is demonstrated
Solid methodology and testing facility are in place
Able to compute type means from 3-5 samples (not shown)
Small discrepancies remain for some antenna models = area of active research
Next Steps
Finalize IGS Antenna Working Group approval
  3-method comparison with Bonn chamber and Geo++ robot is ongoing
  final results to be presented at IGS Workshop in July 2012
Set permanent piers for calibration baseline
Add capabilities to software
  Integrated antenna + receiver units
  GLONASS
Colored lines are azimuthal lines through full PCV pattern every 5. Heavy black line is the NOAZIM elevation-only profile.
NGS solution is shifted to use IGS PCO. Dashed black line is the NOAZIM difference between IGS and NGS values..
IGS minus NGS residuals, shown with respect to azimuth and elevation angle (lefthand circular plots) and as a histogram (righthand). Vertical bars in histogram denote 1mm and 2mm bounds for IGS AWG approval.
We provide NGS PCO values from the individual calibration of the serial number shown on the photo, to demonstrate the NGS method’s ability to correctly recover PCO. However, all further comparison (plots to right) are after shifting NGS values to use the published IGS PCO.
Percentage of NGS-IGS residuals which fall within 1mm and 2mm bounds.
Pre-Edit Phase
Geometric range
Single Difference Phase
Cycle slip editing
Time Difference of Single Difference Phase Pairs
Phase windup
PTU tilt arm
Satellite XYZ/velocity calcs (for windup)
Form / Solve Normal Equations
PCO (east, north, up components)
PCV (elevation and azimuth angle)
Calculation of Angles
Angles in local frame
Angles in antenna frame
Data Collection (all 4 directions)
Samples collected with antenna mounted in north orientation
Composite sampling after all four directions
The 2-axis robot lacks the third degree of freedom necessary to fully sample the PCV pattern. Collecting data with the antenna in 4 different orientations on the robot circumvents this limitation.
… compared to IGS type mean
… compared to other absolute calibration methods
Members of the IGS Antenna Working Group (AWG) are conducting “ring calibrations”, that is, calibrating individual antennas with different systems and environments to test consistency between methods.
N E U
Bonn -0.03 0.50 58.89
Geo++ -0.25 -0.19 58.34
NGS -0.12 -0.17 59.74
[mm] N E U
Bonn 0.71 0.27 67.70
Geo++ 1.01 -0.27 67.70
NGS 1.25 -0.31 67.46
s/n 30213962
Trimble Zephyr 2
TRM55971.00
Histogram of full (azimuth and elevation-dependent) PCV differences between solution pairs. Black vertical bars in histogram denote 1mm and 2mm bounds.
(left) NOAZIM elevation-only PCV profile. (right) differences between solution pairs. All results have been shifted to use common PCO values.
Because this antenna model does not have chokerings, we expect results to be more sensitive to environmental effects such as multipath. Even with this expectation, the different methods have excellent PCO agreement and PCVs agree at < 2mm level.
Geo++: field calibration with 3-axis robot and Kalman filtering
Bonn: anechoic chamber calibration with signal simulator and 2-axis robot
100% < 1mm @ >10
100% < 2mm @ 10
Colored lines are azimuthal lines through full PCV pattern every 5, for the first serial number. Heavy green line is the NOAZIM elevation-only profile, offset by -3 mm for clarity. The heavy dashed black line is the difference between Bonn and NGS NOAZIM values.
Full PCV residuals, Bonn minus NGS .Vertical bars in histogram denote 1mm and 2mm bounds for IGS AWG approval.
Trimble D/M GNSS
TRM59800.00
N E U
0.93 1.08 91.42 1.35 -0.17 91.94
0.29 1.20 121.91
0.69 -0.74 123.19
0.77 0.88 91.51 -0.64 0.33 91.60
1.12 0.62 121.79 -0.58 -0.24 123.16
0.84 1.46 91.56 0.00 1.15 91.63 0.52 0.40 121.93 -1.00 -0.81 122.55
PCO values for three different serial numbers of TRM59800.00 antennas, Bonn in red and NGS in black.
L1
L2
L1
L2
L1
L2